## Slide 1: RF quad tracking study - 2
D. Rubin
November 2, 2017

## Slide 2
Modulate voltage of Q2 short with fRF
CBO frequency depends on momentum, and effectiveness of voltage modulation depends on fCBO – fRF
Single particle with zero position offset but +-0.2% momentum offset

## Slide 3
The most effective RF frequency depends on momentum

## Slide 4
Most effective RF frequency vs muon momentum
Set f_RF= 0.985 for some damping at all momenta with 20 us RF pulse
Near quad plates gradient is small and focusing weak

## Slide 5
RF has no effect on on momentum particles

## Slide 6
Compare effectiveness of RF matching vs Quad scraping
Quad - RF and scraping parameters
Quad voltage 25kV
Quad scraping ramp 18-25 kV
Modulate voltage on Q2 short at afCBO (a ~ 1)
Amplitude of modulation is 5kV
 | Top | Bottom | Inner | outer
Q1 | +25 | +18 | -25 | -25
Q2 | +25 | +18 | -18 | -25
Q3 | +25 | +18 | -25 | -25
Q4 | +25 | +18 | -25 | -18
Scraping parameters

## Slide 7
Gaussian momentum distribution: width= 2%
Emittance = 0
Bunch length=0
Scraping vs RF – RMS width vs time

## Slide 8
Lost muons
Gaussian momentum distribution: width= 2%
Emittance = 0
Bunch length=0

## Slide 9
Gaussian momentum distribution: width= 2%
Emittance = 40 mm-mrad
Bunch length=0

## Slide 10
Gaussian momentum distribution: width= 2%
Emittance = 40 mm-mrad
Bunch length=0
Lost muons

## Slide 11
Emittance = nominal
Dp/p =2%
Length = ‘W’ (zero for scraping config)
Initial displacement = 0

## Slide 12
Emittance = nominal
Dp/p =2%
Length = ‘W’ (zero for scraping config)
Initial displacement = 0
Lost Muons

## Slide 13
Summary
5kV RF modulation of Q2 short at ~ CBO frequency effectively matches dispersion and CBO amplitude of off momentum muons
Chromaticity complicates choice of RF frequency. But if the model is reliable, there is sufficienty bandwidth
Checked with gaussian emittance and momentum and ‘W’ temporal distribution initiated on magic radius
To be checked with
  ‘Real’ distribution starting in ring
  ‘Real’ distribution through injection channel and with kickers